## Slide 2: Digital Electronics 3 Dr. Apurba Kanti Deb Associate Professor
AND, OR and NOT Gates (realization using Diodes and Transistor). NAND and NOR Gates as Universal Gates.

## Slide 3: OR gate
Two or more inputs, only one output. If any one or more inputs are in
‘ON’(1) state output is ‘ON’(1). If all the inputs are ‘OFF’(0) state only then output if ‘OFF’(0)
Boolean expression Y= A+B+C+..
Truth table: for two inputs
A | B | Y=A+B
0 | 0 | 0
0 | 1 | 1
1 | 0 | 1
1 | 1 | 1

## Slide 4: OR gate
Truth table: for three inputs
Circuit Symbol
A | B | C | Y
0 | 0 | 0 | 0
0 | 0 | 1 | 1
0 | 1 | 0 | 1
0 | 1 | 1 | 1
1 | 0 | 0 | 1
1 | 0 | 1 | 1
1 | 1 | 0 | 1
1 | 1 | 1 | 1

## Slide 5: OR gate
Circuit realizing OR gate using diodes and Transistors

## Slide 6: AND gate
Two or more inputs, only one output. If any one or more inputs are in
‘OFF’(0) state output is ‘OFF’(0). If all the inputs are ‘ON’(1) state only then output if ‘ON’(1)
Boolean expression Y= A.B.C..
Truth table: for two inputs
A | B | Y=A.B
0 | 0 | 0
0 | 1 | 0
1 | 0 | 0
1 | 1 | 1

## Slide 7: AND gate
Truth table: for three inputs
Circuit Symbol
A | B | C | Y
0 | 0 | 0 | 0
0 | 0 | 1 | 0
0 | 1 | 0 | 0
0 | 1 | 1 | 0
1 | 0 | 0 | 0
1 | 0 | 1 | 0
1 | 1 | 0 | 0
1 | 1 | 1 | 1

## Slide 8: AND gate
Circuit realizing AND gate using diodes and transistors

## Slide 9: NOT gate
Only one input, only one output. If inputs is in
‘OFF’(0) state output is ‘ON’(1) & If the input is in ‘ON’(1) state then output if ‘OFF’()
Boolean expression Y=
Truth table:
Circuit symbol:
A | Y=
0 | 1
1 | 0
A | 
0 | 1
1 | 0

## Slide 10: NOT gate
Circuit using Transistors

## Slide 11: NAND gate
Two or more inputs, only one output. If any one or more inputs are in
‘OFF’(0) state output is ‘ON’(1). If all the inputs are ‘ON’(1) state only then output if ‘OFF’(0)
Boolean expression Y=
Truth table: for two inputs
from truth table Y= + (bubbled or gate) De Morgan’s theorem 2
A | B | Y=
0 | 0 | 1
0 | 1 | 1
1 | 0 | 1
1 | 1 | 0
A | B | 
0 | 0 | 1
0 | 1 | 1
1 | 0 | 1
1 | 1 | 0